## Slide 1: Photon Counting Interferometry to Detect Geotropic Space-time Fluctuations with GQuEST
Daniel Grass

## Slide 2: Quantum Mechanics and General Relativity
Quantum Mechanics and General Relativity make very accurate predictions in their own realms
These two theories are incompatible
Many theories exist, like String Theory, LQG, etc, but either don’t make testable predictions or their predictions have not been supported by experiment
Holographic quantum gravity theories point to detectable spacetime fluctuations

## Slide 3: The Proposed Signal
Spacetime Metric modified with a scalar field
Important Features: low amplitude, high frequency, stochastic, and has medium-range spatial correlations

## Slide 4: Problematic for 3rd Generation GW Detectors
Bub et al., 2023

## Slide 5: The Detector

## Slide 6: What if we could build a detector limited by classical noise instead of shot noise?
Notes: Noise budget
Shot noise, purple dotted line, way above signal
Classical noise near signal

## Slide 7: Problems with Homodyne
Homodyne is used in LVK detectors to sense amplitude and phase
However, for excess power measurements, Homodyne is no longer optimal
Homodyne readout’s sensitivity is limited by the shot noise
What is a better readout scheme for excess power measurements?
Danilishin & Khalili, 2012
Notes: James Gardner next

## Slide 8: Photon Counting
Consider an interferometer with no classical noise operated perfectly at the dark port
All photons are signal photons!
Much shorter integration time
Time for SNR of 1 with Fringe Readout: s
= 1 week
Time for SNR of 1 with Photon Counting: s

## Slide 9: But there is carrier light and classical noise
An interferometer can’t be operated at the dark fringe
Conditions of a perfect interferometer can be mimicked with a series of narrow optical band pass filters
Time for SNR of 1 with Filtered Photon Counting: s = 2.4 hours
Notes: James Gardner’s talk will follow mine

## Slide 10: GQuEST Configuration
Using a power-recycled Michelson interferometer
Photon counting readout scheme
Can still collect data with homodyne readout and use it for feedback control
10 W input, 10 kW circulating power, 100 mW output power
1550 nm light for use with Silicon Optics
5 m

## Slide 11: Noise Budget
Dominated by thermal noise from the optics: coating and bulk
To reduce bulk noise, use thin, stiff, and high Q optics
High thermal conductivity desirable to limit thermal lensing
Silicon: stiff, high Q, high thermal conductivity
Notes: Go through noise sources
Mention that we aren’t including noises that LIGO has to deal with, like quantum backaction, seismic, or residual gas, but we have modeled them

## Slide 12: 4 Requirements for Photon Counting
Carrier suppression
Low Dark Count Rate Detector
Low Classical Noise
Small Contrast Defect
4 Optical Bandpass Filters with 22 orders of magnitude suppression in power
Single Photon Detector (SNSPD)
Detector R&D
Excellent Controls and additional R&D

## Slide 13: Optical Bandpass Filters
6 orders of magnitude of carrier suppression each
Bowtie Cavity Configuration
4 cavities in total to suppress carrier
Multiple cavities also prevent higher-order spatial modes and frequency modes from leaking through
25 kHz integrated bandwidth
Locked using 775 nm light
Notes: Say that this mechanically holds the optics

## Slide 14: SNSPD: Superconducting Nanowire Single Photon Detector
Used at the end of the Photon Counting Readout
Aiming for a Dark Count Rate an order of magnitude below the signal level (which would be Hz)
Requires temperatures as low as 0.8 K

## Slide 15: Full GQuEST Configuration
Classical Noise still above Signal
Two phase-locked, co-located Power Recycled Interferometers to cross-correlate
Assuming stationarity of signal and noise, only need one photon counting readout
Can switch whether the output has just noise or signal + noise
Potentially limited by noise at BS-C

## Slide 16: Highlight of other topics
Custom Mirror Mount to hold optics and mode match by correcting for astigmatism
Laser Filter Cavity to reduce laser phase noise and act as a reference for other cavities
Very beginning of work to make bandpass filters with atomic transitions

## Slide 18: Thank you!

## Slide 19: Extra Slides

## Slide 20: Spacetime Fluctuations in LIGO
Bub et al., 2023
Notes: Livingston detector, alpha = 1

## Slide 21: More on Optical Bandpass Filters
Finesse of 3000
FSR of 125 MHz (2.4 m long)
42 kHz individual bandwidth
Round Trip Guoy phase of
10 ppm loss per mirror: 98% signal transmission
Allow for an effective signal band between 8 MHz and 40 MHz

## Slide 22: Bowtie Cavity Laser Design

## Slide 23: Laser Filter Cavity Justification

## Slide 24: Custom Mirror Mount Design

## Slide 25: Custom Mirror Mount Simulation

## Slide 26: Eigenmode Decomposition Theory
The mirror has (many) eigenmodes
Each eigenmode displaces the mirror surface, which affects the phase of the light and looks like signal
The strength of the noise from each eigenmodes is proportional to the overlap integral of the beam and the eigenmode

## Slide 27: What are these modes?
Longitudinal
Transverse

## Slide 28: Better Filter Justification

## Slide 29
“Quantum Gravity” measurement limit
(Standard Quantum Limit)
(‘Schwarzschild limit’)
Sander M. Vermeulen
Jack Ng & Van Dam (1994)

## Slide 30
Limits on distance measurements from Quantum Gravity
Sander M. Vermeulen
EFT/String Theory/ LQG
Hoop Conjecture/ ‘Old’ holography (Y. Jack Ng & Van Dam)
Random walk, ‘New’ holography (Zurek & Verlinde, Hogan & Kwon)

## Slide 31
Light cone fluctuations accumulate like a random walk
Sander M. Vermeulen
space
time
Step size:
Number of steps
Total length:
Verlinde & Zurek (2019)
Hogan (2012)
Can we detect displacements m ?